## Slide 1
UNDERGRADUATE RESEARCH · EE 28499 · SPRING 2026
Uncertainty & LLM-Guided
Environment Generation
for NeuroCotans
Amir Tomashpayev
Student
Prof. Toros Arikan
Advisor · Wireless Institute
UNIVERSITY OF NOTRE DAME · DEPARTMENT OF ELECTRICAL ENGINEERING

## Slide 2
THE PROBLEM
Where is that boundary, and how sure are we?
A sonar pulse goes out.
It bounces off something underwater.
We hear an echo.
Where exactly was the surface?
NeuroCotans answers with two numbers: ρ (distance, 0–10 m) and θ (angle, 0–360°).
receiver
boundary
ρ
θ
ρ = distance θ = bearing
NeuroCotans · Amir Tomashpayev · Spring 2026
2 / 9

## Slide 3
THE PIPELINE
From acoustic echo to a confident prediction
1
Sonar measurement
raw acoustic data
›
2
COTANS transform
101×360 heatmap
›
3
Trained UNet
segmentation
›
4
Boundary location
(ρ, θ) output
CONTRIBUTION 1
LLM-guided environment generation
CONTRIBUTION 2
MC Dropout uncertainty estimation
NeuroCotans · Amir Tomashpayev · Spring 2026
3 / 9

## Slide 4
FOUNDATION · FEB – MAR
What makes an environment valid?
The first task wasn't ML at all.
Vary boundary distance, angle, count, and separation. Generate hundreds of COTANS images. Report which configurations the network can actually read.
The criteria I extracted became the validity ruleset I later fed to the LLM.
KEY FAILURE MODE
Left: two distinct bright peaks the network can read.
Right: boundaries placed too close — peaks merge into one blurry region.
Output: a concrete validity ruleset.
NeuroCotans · Amir Tomashpayev · Spring 2026
4 / 9

## Slide 5
CONTRIBUTION 1 · APRIL
An LLM that generates valid environments
THE SETUP
Local Llama via Ollama — runs on the lab machine, no API.
Validity ruleset as the system prompt.
Structured JSON output → straight into the simulator.
FOUR SPATIAL TESTS
01
One per region
02
Range split 3–4 vs 7–9 m
03
Opposite sides
04
Close pair, > 80° apart
2 of 4 LLM-generated scenarios · COTANS image (left) → ground truth (right)
4 / 4 scenarios on first call · but ~700× slower than random
NeuroCotans · Amir Tomashpayev · Spring 2026
5 / 9

## Slide 6
CONTRIBUTION 2 · APRIL
MC Dropout — uncertainty for free
THE GAP
NeuroCotans always outputs a prediction —
but never says how much to trust it.
ρ = 4.2 m, θ = 127° looks identical whether the network is certain or completely guessing.
THE TRICK
1. Keep dropout ON at inference.
2. Run the same image 30 times.
3. Spread of predictions = uncertainty.
30 PASSES, SAME INPUT
CONFIDENT
UNCERTAIN
ZERO RETRAINING
The trained UNet already has 18 Dropout2d layers. Three lines flip them on at inference.
NeuroCotans · Amir Tomashpayev · Spring 2026
6 / 9

## Slide 7
CONTRIBUTION 2 · EXPERIMENT 1
Uncertainty predicts error
THE EXPERIMENT
60 environments · 30 MC passes each
For every image, plot the spread of the 30 predictions against the actual error vs ground truth.
PEARSON CORRELATION
r = 0.83
The network reliably signals when it will be wrong.
NeuroCotans · Amir Tomashpayev · Spring 2026
7 / 9

## Slide 8
CONTRIBUTION 2 · EXPERIMENT 2
Where in the image is the network unsure?
THREE COLUMNS
1. COTANS input
the heatmap fed to the network.
2. Mean prediction
average of 30 segmentations.
3. Pixel-wise std dev
exactly where the network is unsure.
Top row uncertainty = 0.6 m·° · Bottom row uncertainty = 59.6 m·° · same architecture, same weights, no retraining.
NeuroCotans · Amir Tomashpayev · Spring 2026
8 / 9

## Slide 9
CLOSING
Two takeaways · Live demo
TAKEAWAY 1
LLMs understand domain rules
…but won't outpace simple random sampling in a well-constrained parameter space. Useful as a steerable interface, not a speed-up.
TAKEAWAY 2
The trained model already knew
Useful uncertainty information was sitting inside the existing UNet — extractable at zero retraining cost, including OOD detection.
LIVE DEMO
Streamlit app
Drag the SNR slider
Generate a new environment
Watch the uncertainty react
▶
streamlit run amir/streamlit_demo.py
Thank you · Questions?